GEOMETRY

(Kares DP1998 reports slightly different values,

e.g. distance of PT100 130mm).

Internal volumes

According to Novy M., 2000 (measured)

Tank (with balsa inserts)	… 2,53543 l

Inner volume between conductivity detectors (with 10mm balsa )		… 3,027 l

Inner volume between conductivity detectors (without balsa )			… 3,980 l

Calibration of flow-rate through modified slits

Measured 16.3.2001 by Zitny

Method of measurement

Pressure drop	(p=2400 Pa (240 mm H2O)

V=5.10-5 m3

time t=12-18 s, average 15 s.

Volumetric flowrate

Cross section, mean velocity and dynamic pressure drop

SWide = 0.01 x 0.002=0.00002 m2, velocity u=0.167 m/s, (p=0.5(u2=14 Pa

Snarrow=0.01 x 0.0002=0.000002 m2, velocity u=1.67 m/s, (p=0.5(u2=1400 Pa

# Text boxes

Geometry of perforated electrode.

7.8

80.5

36.4(0.2

18

PT21-Reflex

balsa (10mm)

78

10

590

60

185

310

435

560

250

162

162

8

78

18

T5

T3

T4

T2

T1

PT3

PT4

3 mm

0.2 mm

2 mm

Stop watch

Silicon hose