Matlab for Simulations
Stanislav Vrána
Systems of differential equations
Transfer function

---
Poznámky
- http://www.sharetechnote.com/html/DE_Modeling_Example_SpringMass.html
- http://multimedia08.zcu.cz/en_mpero.htm
- http://www.efunda.com/formulae/vibrations/sdof_free_undamped.cfm
- http://www.352.vsb.cz/uc_texty/AutoRizMatlab/kap211.html
- http://12000.org/my_notes/simulink_second_degree/index.htm
- http://12000.org/my_notes/simulink_second_degree/index.htm

---
Spring

---
Spring

---
Spring equation
The inner damping force can be very small, so it is possible to consider β = 0. If necessary, the inner damping can be modelled as external damping. Then, if the spring is loaded by external force F(t)
size 50 { "k"x(t) = F(t) }
size 50 { k left ( x(t) right ) x(t) = F(t) }

---
Spring and mass
Spring – mass system
F
size 50 { m ddot x(t) + "k"x(t) = F(t) } newline newline size 50 { ddot x(t) = {F(t) - "k"x(t)} over m }

---
Spring and mass

---
Spring and mass

---
Spring and mass

---
Spring and mass

---
Spring and mass
Till now, only the difference between the length of spring when unloaded and loaded by force is shown. But it is necessary to verify if current spring length does not exceed the limits.

---
Spring and mass
l0 = 1.5, lmin = 0.6

---
Spring and mass with damping
Spring – mass – damping system
size 35 { m ddot x(t) + "b" dot x(t)+ "k"x(t) = F(t) } newline newline size 35 { ddot x(t) = {F(t) - "b" dot x(t)- "k"x(t)} over m }

---
Spring and mass with damping

---
Conversion of differential equation system
First step is separation of the highest derivations in all equations.
size 50 { dddot y + 3 ddot y + 2 dot y + y + dot z = u } newline size 50 { ddot z + 2 dot z + z + y = v }
size 50 { dddot y = u - 3 ddot y - 2 dot y - y - dot z } newline size 50 { ddot z = v - 2 dot z - z - y }

---
Conversion of differential equation system
Then it is suitable to prepare all variables into scheme.
size 30 { dddot y = u - 3 ddot y - 2 dot y - y - dot z } newline size 30 { ddot z = v - 2 dot z - z - y }
The equation systém is suitable convert as a set of independent equations and connect them in final step. The possible mistakes can be found more easily.

---
Conversion of differential equation system
Then it is suitable to prepare all variable into scheme.
size 30 { dddot y = u - 3 ddot y - 2 dot y - y - dot z } newline size 30 { ddot z = v - 2 dot z - z - y }