## Slide 1
Žitný BC project for Glasgow students 2015 (frozen since September 2015)
RZ10
Metzner White convergent/divergent Gauss planar channel flow
GAČR = kolagen
Motto: It is a big mistake for teachers that they do not ask students about their dreams and ideas before creative genes of pure-minded students came under the tutelage of tutors. And an even bigger mistake is when the students afraid to talk about their crazy ideas.

## Slide 2
History of project
The idea, how to determine the relaxation time of viscoelastic fluid by comparing the pressure drop at elongation and compression flows in a converging/diverging slot, think about everyone after reading the first book about rheology. The problem is in a technical realization of viscoelastic stresses measurement along a channel with a variable cross section: Possible solution was to use the concept of groove strain-gauge sensors for measuring the axial pressure profile in the annular gap of existing extrusion rheometer (the development of these sensors was implemented from the beginning of the seventies). The first practical experiments (convergent/divergent gap between the cylindrical tube with attached sensors and internal double-cone pin) were up in the early nineties. Relevant results were summarized in Pavlovec thesis (theoretical solution assuming the analytic velocity profiles corresponding to a power fluid flow and numerical solutions of viscoelastic fluid type Metzner White) and in thesis by Zeleny (experiment with collagen and a double-cone pin - certain differences in pressure losses in the convergent/divergent slit were recorded). Mr. Pavlovec was an excellent student, but its thesis has not been completed (Fortran programs did not converged and the result was reduced to extremely simplified 1D analysis). The problem is simply too complicated for single student without sufficient background. And that is the true goal of this presentation: to prepare a groundwork for english speaking students from Glasgow.

## Slide 3
History of project
Previous presentation RZ8 was almost duplicated thesis of Pavlovec, programmed in MATLAB with certain exemptions in differencing (but basic simplification consisting in using the power law velocity profile, was preserved). Although solutions converge, the results raise some doubts, especially the occurrence of strange peaks of calculated pressures in the axis of the channel and also the unexpected effect of elasticity: Pressure loss in the convergent section was lower than in the divergent section (see following sheet No. 13). Independent solutions and programming performed by student (Mr. Frouz) reportedly received identical results (presented at the Students Conference). Still, I'd be very happy if he could express his findings in the form of diagrams on a slide 13, so that a consensus was evident.
Stretched fiber
Compressed fiber
Equilibrium fiber
The following diagram is a visualization of what's happening with a loaded fiber. According to this concept the normal stress on the wall should be lower than during the stretching of the fiber during its compression. But it is at odds with the results of the model (see sheet 7).
This visualization is perhaps misleading (it say that the normal stress in the zone of elongation is less than in the compression zone), because the de-facto ignores the influence of time. I will be grateful to anyone who offers a better interpretation of what was really going on polymer fibers.

## Slide 4
History of project discussion of simplifying assumptions (assumed velocity profile not affected by elastic forces)
RZ8 model assuming linear cross-sectional profile of convergent/divergent slots along with the assumption of a power law velocity profile actually result to a discontinuity of elongation rate (positive constant rate of elongation in the convergent zone while a constant negative rate in the divergent zone). The discontinuity and weak singularity at the transition may cause unrealistic peak pressures and inaccuracies axial profile of normal stresses. These fundamental shortcomings could be eliminated using the model described in this presentation. The axial cross-sectional profile channel (and therefore the rate of elongation) is a smooth function (Gaussian curve), and the velocity field is calculated (based on the concept of the current function and vorticity). Technically speaking, the manufacture of the walls with the Gaussian profile should be no problem (using rapid prototyping - the geometry of the channel varies exchanging inserts, which must anyway be of non-conductive plastic which is then glued strips electrodes). The disadvantage is the computational complexity of relationships and the possibility of an error (because in this presentation are reported in respect of each field checked .... ..).
Kontroloval: xxxxx
Solution flow of viscoelastic fluid in a convergent / divergent slot can also be simulated by existing commercial software (Polyflow ANSYS) and OpenFOAM. These project can be alternatively solved by other Glasgow students. The ideal would be a comparison of approaches - it is a matter of debate.

## Slide 5
Literature
Crochet M.J., Davies A.R., Walters K.: Numerical simulation of non-Newtonian flow. Elsevier 1984
Pavlovec J.: Výtlačný reometr pro viskoelastické kapaliny. Dipl.práce, ČVUT FS, 1991
Anderson J.D.: Computational Fluid Dynamics. McGraw Hill, Inc., N.Y., 1995
Owens R.G., Phillips T.N.: Computational Rheology. Imperial College Press, London 2002
Davidson et al. Velocity and stress fields of polymeric liquids flowing in a periodically constricted channel. J. Non-Newtonian Fluid Mech. 49 (1993)
Baird D.G. First normal stress difference measurements…., J. Non-Newtonian Fluid Mech. 148 (2008)
Baaijens F. Mixed FEM for viscoelastic flow analysis, a review. J. Non-Newtonian Fluid Mech. 79 (1998)
James D.F., Chandler G.M.,Armour S.J. : A converging channel rheometer for the measurement of extensional viscosity. Elsevier 1998 (mam jen papirovou kopii bez bibl.udaju)
James D.F., Chandler G.M., Armour S.J. : Measurement of the extensional viscosity of M1 in a converging channel rheometer. J. Non-Newtonian Fluid Mech. 35 (1990)
Han Chang Dae: Measurement of the rheological properties of polymer melts with slit rheometer I.Homopolymer systems. J.Applied Polymer Science, 15 (1971)
Davies J.M. et al: Theory for normal stresses in slits and capillaries. J. Phys. D. : Appl.Phys, Vol.6 (1973), 2259-2266
Cogswell F.N. Converging flow of polymer melts in extrusion dies. Polymer Engngr. and Sci. (1972)
Cogswell F.N. Converging flow and stretching flow a compilation. J. Non-Newtonian Fluid Mech. Vol.4 (1978), 23-38
Binding D.M. An approximate analysis for contraction and converging flows. J. Non-Newtonian Fluid Mech. Vol.27 (1988), 173-189
Additional papers

## Slide 6
Diploma work J.Pavlovec: Výtlačný reometr pro viskoelastické kapaliny. 1991
Adviser R.Žitný, oponent M.Houška
Constitutive model UCM (upper convective Maxwell) modification White-Metzner
Convergent section with positive elongation
Divergent section compression of fibers
Relaxation time
Viscosity
Only INFO old presentation RZ8 (skip)

## Slide 7
Vague idea of Maxwellian model (maxwell.xlsx)
Particular solution
General solution
Effect of relaxation time  increase to axial stress profile  (, 2, 5)
relaxation time [s]
Vague because it does not specify the nature of the stress  (imagine that it is for example an elongation stress in the direction of flow). The model considers a linear change in velocity u and strain rate  along a channel.
Weissenberg number (elasticity number) = relaxation time * rate of deformation

5
Only INFO old presentation RZ8 (skip)

## Slide 8
Pavlovec : dimensionless parameters
Transformation into an orthogonal coordinate system
L
H
L
LI
L
L
LI
x
H
Inlet section Convergent section Divergent section
Transformation of derivatives
Kontroloval: Frouz
Kontroloval FROUZ
Only INFO old presentation RZ8 (skip)

## Slide 9
Power law approximation of velocities
Axial velocity
Transversal component (satisfying continuity equation )
Kontroloval FROUZ
Only INFO old presentation RZ8 (skip)

## Slide 10
Power law approximation of viscosity
Viscosity as a power function of the second invariant
Rate of deformation in the dimensionless coordinates (0,1), (0,1)
Kontroloval FROUZ
Only INFO old presentation RZ8 (skip)

## Slide 11
Constitutive equation White Metzner
An important conclusion: the lower flat plate is yy = 0, which means that the pressure sensor measures the isotropic pressure p
Kontroloval FROUZ
Only INFO old presentation RZ8 (skip)

## Slide 12
Pressure distribution by integration Cauchy equations from left. Results
% white metzner - velocities
% rychlosti ux(1:nx,1:ny),uy(1:nx,1:ny),
% derivace duxdksi(1:nx,1:ny), duxdeta(1:nx,1:ny), duydksi(1:nx,1:ny), duydeta(1:nx,1:ny)
% duxdx(1:nx,1:ny), duxdy(1:nx,1:ny), duydy(1:nx,1:ny), duydx(1:nx,1:ny)
% viskozity mju(1:nx,1:ny)
% beta, dl, h0, n, vdot, K G koeficient konzistence a modul G
%main white-metzner
clear all;
K=100;
n=0.5;
nx=59;
ny=37;
dl=0.2;
h=0.005;
h0=h;
dh=0.004;
um=0.1;
vdot=um*h0*(n+1)/(2*n+1)
G=5000
beta=0;
uxy;
for i=1:nx
pp(i)=pav(i);
x(i)=(i-1)*dl/(nx-1);
end
beta=-dh/h0;
uxy;
ig=nx;
ig0=ig;
for i=2:nx
ig=ig+1;
pp(ig)=pav(i);
x(ig)=(ig-1)*dl/(nx-1);
end
ig1=ig;
h0=h-dh;
beta=dh/h0;
uxy;
for i=2:nx
ig=ig+1;
pp(ig)=pav(i);
x(ig)=(ig-1)*dl/(nx-1);
end
ig2=ig;
figure(1)
plot(x(1:ig2),pp(1:ig2))
hold on
plot(x(ig0),pp(ig0),'ro')
plot(x(ig1),pp(ig1),'ro')
plot(x(ig2),pp(ig2),'ro')
d1=pp(ig0)-pp(ig1);
d2=pp(ig1)-pp(ig2);
drel=(d1-d2)/max(abs(d1),abs(d2));
disp(sprintf('dp conv=%0.5g dp div=%0.5g dif=%0.5g',d1,d2,drel));
title(sprintf('G=%0.5g diff=%0.5g Vdot=%0.3g',G,drel,vdot))
xlabel('x [m]')
ylabel('p [Pa]')
Peek pressure on the axis of the channel is about an approximation error
Only INFO old presentation RZ8 (skip)

## Slide 13
Axial pressure profiles p(x) (n=0.5, K=100, V=0.000375 m2/s)
The graphs show what happens when you grow modulus G (resp. While reducing the relaxation time). Small values G represent great influence elasticity (pressure gradient in the convergent gap is then smaller than the divergent)
G = 5000 negligible elasticity, different pressures are error of approximation
W=10
W=0.4
W=2
W=4
W=18
Commented presentation RZ8

## Slide 14

Stream function, vorticity, elastic stresses

s

## Slide 15
Stream function, vorticity, elastic stresses
Geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stresses sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Nodal velocities and viscosity. BC for 
This is rather complicated project probably too difficult for batchelor or even diploma work.
However it can be significantly simplified by skiping the solution of flow , (assuming only velocity approximation) and neglecting viscosity variation.

## Slide 16
Gaussian axial profile of gap
The reason for choosing the smooth profile of the upper walls: the exclusion of the weak singularity at a sharp edge between converging and diverging axial channel crossection
x
y
Physical domain
i,j
i,j+1
i,j-1


Computational domain
Transformation of coordinates (x,y) (x,y)
and metric coefficients
necessary for transformation of first and second order derivatives

## Slide 17
Gaussian axial profile of gap Metric coefficients of first derivatives
x
y
Lk
Ld
h
H
=0
=1
Transformation from computational domain (0,2) (0,1) to physical domain x(0,Lk+Ld), y(0,H)
Dimensionless geometric parameters
=
=
=
=

Kontroloval Zitny

## Slide 18
Gaussian axial profile of gap Metric coefficients of second derivatives
Because  depends upon x only linearly the second derivatives of  are zero




Kontroloval: zitny
Only two derivatives of transversal coordinate  are nonzero
Ověřeno numerickými diferencemi

## Slide 19
INIT calculation of metric coefficients
Geometrie h, H, Lk, Ld, , Nx, Ny
INIT
ksi=linspace(0,2,nx);
eta=linspace(0,1,ny);
i=1,2..Nx
J=1,2..Ny
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 20
INIT.m calculation of coefficients (MATLAB)
clearvars
um=0.1;n=0.5;K=100;
H=0.005;h=0.001;Lk=0.2;Ls=0.2;delta=0.1;
lambda=Lk/delta;
kappa=h/H;
nx=201;
ny=41;
ksi=linspace(0,2,nx);
eta=linspace(0,1,ny);
x=Lk*ksi;
for j=1:ny
for i=1:nx
E=exp(-(Lk/delta)^2*(ksi(i)-1)^2);
y(i,j)=eta(j)*H*(1-(1-kappa)*E);
end
end
%derivace transformaci
for i=1:nx
E=exp(-(lambda*(ksi(i)-1))^2);
for j=1:ny
k1=1-(1-kappa)*E;
dksidx(i,j)=1/Lk;
detadx(i,j)=eta(j)*(1-kappa)*E*2*lambda^2*(1-ksi(i))/(k1*Lk);
detady(i,j)=1/(k1*H);
detadxdy(i,j)=(1-kappa)*2*lambda^2*(1-ksi(i))*E/(H*Lk*k1^2);
detadxdx(i,j)=2*lambda^2*eta(j)*(1-kappa)*E/(Lk^2*k1)*(2*lambda^2*(1-ksi(i))^2*(1+(1-kappa)*E)/k1-1);
gxx(i,j)=dksidx(i,j)^2; gyy(i,j)=detadx(i,j)^2+detady(i,j)^2; gxy(i,j)=2*detadx(i,j)*dksidx(i,j); gx(i,j)=detadxdx(i,j);
end
end
%figure(2)
%surf(eta,ksi,detadx)
%title('deta/dx')
Matrices defined at INIT
x(nx), y(nx,ny) kartézské souřadnice
ksi(nx),eta(ny) výpočtová doména
dksidx(nx,ny),detadx(nx,ny),detady(nx,ny) /x, /x,
detadxdy(nx,ny),detadxdx(nx,ny) 2/xy, 2/x2,
gxx(nx,ny),…gx(nx,ny)
Matrices defined later
psi(nx,ny), omega(nx,ny)
u(nx,ny),v(nx,ny),dudx(nx,ny),dudy(nx,ny),dvdx(nx,ny),dvdy(nx,by)
mju(nx,ny),dmjudx(nx,ny), dmjudy(nx,ny), dmjudxdy(nx,ny), , /x, /y,
Approximation for power law fluid
psin(nx,ny), omegan(nx,ny)
un(nx,ny),vn(nx,ny),dudxn(nx,ny),dudyn(nx,ny),dvdxn(nx,ny),dvdyn(nx,by)
mjun(nx,ny),dmjudxn(nx,ny), dmjudyn(nx,ny), dmjudxdyn(nx,ny),
Stresses
sxx(nx,ny), syy(nx,ny), sxy(nx,ny),
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 21
Transformation of derivatives of quantity F (e.g. , , sxx, syy, sxy)
Transformation of first derivative
Transformation of second derivatives (derivation is a bit lengthy)
Kontroloval: zitny
... it would be possible to express the transformation of derivatives also in the reverse direction, but usually we do not need this

## Slide 22
Cauchy equations with consideration of inertia forces
Elimination of pressure by introducing the vorticity and using the continuity equation
Fulfill the continuity equation by introducing the current function
The result is the transport equation of vorticity (right side resultant stress). At zero Re (creeping flow, 0) the left side is zero and vorticity disappears from this equation.
Kontroloval: zitny

## Slide 23
Initial conditions - stream function (for a power law fluid)
Stream function (,)
Velocity components u,v (,)
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 
Velocities calculated in this way satisfy continuity equation and correspond to the steady creeping flow of power law fluid (without elastic effects). It is assumed that these initial conditions can be applied also as boundary conditions at inlet and outlet (far from the disturbance of throat).

## Slide 24
Initial conditions - stream function (for a power law fluid)
Section corresponding to the distance from the entrance =x/Lk
Stream function (um is maximum velocity for the gap thickness H). It holds umH=umH .
Corresponding velocity components
Kontroloval: zitny

## Slide 25
Initial conditions – vorticity (for a power law fluid)
Vorticity
Auxilliary variables
corresponds to the direction anti-clockwise
Kontroloval: zitny
Verified by three methods: analytically, direct numerical difference and differential transformed derivatives (it took me few days to match the threee procedures

## Slide 26
Initial conditions – viscosity (for a power law fluid)
Auxilliary variables
Kontroloval: zitny
Verified numerically
Dangerous peeks correspond to regions with smal velocity gradients (this is disadvantage of power law model)
Analytical expressions for first derivatives are too complicated and will be approximated numerically

## Slide 27
Initial conditions – POWER.m (MATLAB code 1/2)
for i=1:nx
Ek=exp(-lambda^2*(1-ksi(i))^2);
Hk=H*(1-(1-kappa)*Ek);
for j=1:ny
Z=1-2*y(i,j)/Hk;
HK=H/Hk;
psi(i,j)=um*H/2*(1-Z-n/(2*n+1)*(1-sign(Z)*abs(Z)^((2*n+1)/n)));
u(i,j)=um*H/Hk*(1-abs(Z)^((n+1)/n));
v(i,j)=-2*um*(lambda*H/Hk)^2*(1-Hk/H)*(1-ksi(i))*y(i,j)/Lk*(1-abs(Z)^((n+1)/n));
dudy(i,j)=2*um*H/Hk^2*(n+1)/n*sign(Z)*abs(Z)^(1/n);
F=(HK^2-HK)*(1-abs(Z)^((n+1)/n));
dHkdx=2*H*lambda^2*(1-kappa)*(ksi(i)-1)*Ek/Lk;
dFdHk=H/Hk^2*((-2*HK+1)*(1-abs(Z)^((n+1)/n))-sign(Z)*(HK-1)*(n+1)/n*abs(Z)^(1/n)*(1-Z));
dvdx(i,j)=-2*um*lambda^2*y(i,j)/Lk*(dFdHk*dHkdx*(1-ksi(i))-F/Lk);
omega(i,j)=dvdx(i,j)-dudy(i,j);
dudx(i,j)=-2*um*(HK*lambda)^2*(1-kappa)*(ksi(i)-1)*Ek/Lk*(1-abs(Z)^((n+1)/n)+sign(Z)*(n+1)/n*abs(Z)^(1/n)*(1-Z));
dvdy(i,j)=-2*um*(HK*lambda)^2*(1-1/HK)*(1-ksi(i))/Lk*(1-abs(Z)^((n+1)/n)+sign(Z)*(n+1)/n*abs(Z)^(1/n)*(1-Z));
mju(i,j)=K*(2*dudx(i,j)^2+2*dvdy(i,j)^2+(dudy(i,j)+dvdx(i,j))^2)^((n-1)/2);
end
end
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 
Velocities, stream function, vorticity, viscosity for power law fluids

## Slide 28
Initial conditions – POWER.m (MATLAB code 2/2)
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 
dmjudx(1:nx,1:ny)=0; dmjudy(1:nx,1:ny)=0;
for i=2:nx-1
for j=2:ny-1
dmjudx(i,j)=(mju(i+1,j)-mju(i-1,j))/(2*hx)*dksidx(i,j)+(mju(i,j+1)-mju(i,j-1))/(2*hy)*detadx(i,j);
dmjudy(i,j)=(mju(i,j+1)-mju(i,j-1))/(2*hy)*detady(i,j);
end
end
for i=1:nx
dmjudx(i,1)=dmjudx(i,2);
dmjudx(i,ny)=dmjudx(i,ny-1);
end
for j=1:ny
dmjudx(1,j)=dmjudx(2,j);
dmjudx(nx,j)=dmjudx(nx-1,j);
end
% copy matrices
psin=psi; omegan=omega; un=u; vn=v;
dudxn=dudx; dudyn=dudy; dvdxn=dvdx; dvdyn=dvdy;
mjun=mju; dmjudxn=dmjudx(nx,ny); dmjudyn=dmjudy;
Approximation of viscosity derivatives

## Slide 29
PSI Transformation of stream function into computational domain
Poisson equation for stream function can be transformed into computational domain using previously calculated metric coefficients
Kontroloval: zitny

## Slide 30
PSI Discretization of stream function
i,j
i,j+1
i,j-1


=0
=1
=0
=1
=2
hx
hy
Kontroloval: xxxxxx

## Slide 31
PSI by alternation direction implicit method (ADI) Time evolution approximation
PSI
i=2..Nx-1
iter=1,2,…
Sweep of tridiagonal system for  in vertical direction (sections i)
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 
Norm of difference new-old and repetition the PSI loop
i=2..Nx-1
Sweep of tridiagonal system for  in horizontal direction (only smoothing)
This horizontal sweep doesn’t work correctly. Maybe because  is almost independent on 

## Slide 32
PSI Discretization of stream function (time marching)
Kontroloval: xxxxxx
-implicit (horizontal lines)
-implicit (vertical lines)
gxx … coefficients were calculated during INIT.m
This part (-implicit step) does not work at tests
It was substituted by a simple filter, see the source code

## Slide 33
PSI Discretization of stream function PSIE.m (MATLAB)
Kontroloval: xxxxxx
dt2=(H/ny)^2*1e3; dt1=(Lk/nx)^2*1e3;
psiold=psi;
for iter=1:20
% horizontal lines (only smoothing)
for j=2:ny-1
aa(1)=0;bb(1)=1;cc(1)=0;dd(1)=psi(1,j); aa(nx)=0;bb(nx)=1;cc(nx)=0;dd(nx)=psi(nx,j);
for i=2:nx-1
aa(i)=-gxx(i,j)/hx^2; bb(i)=1/dt1+2*gxx(i,j)/hx^2; cc(i)=-gxx(i,j)/hx^2; dd(i)=psi(i,j)/dt1;
end
psi(1:nx,j)=tridag(aa,bb,cc,dd,nx);
end
% vertical lines
for i=2:nx-1
aa(1)=0;bb(1)=1;cc(1)=0;dd(1)=psi(i,1); aa(ny)=0;bb(ny)=1;cc(ny)=0;dd(ny)=psi(i,ny);
for j=2:ny-1
aa(j)=-gyy(i,j)/hy^2+gx(i,j)/(2*hy); bb(j)=1/dt2+2*gyy(i,j)/hy^2; cc(j)=-gyy(i,j)/hy^2-gx(i,j)/(2*hy);
ddxx=gxx(i,j)/hx^2*(psi(i-1,j)-2*psi(i,j)+psi(i+1,j)); ddxy=gxy(i,j)/(4*hx*hy)*(psi(i+1,j+1)+psi(i-1,j-1)-psi(i-1,j+1)-psi(i+1,j-1)); ddomega=omega(i,j);
dd(j)=psi(i,j)/dt2+ddxx+ddxy+ddomega;
end
psi(i,:)=tridag(aa,bb,cc,dd,ny);
end
% norm of differences
sum=0;
for i=1:nx
for j=1:ny
sum=sum+abs(psi(i,j)-psiold(i,j));
end
end
sdev=sum/(nx*ny)/psiw;
disp(sprintf(' iter=%d relsum=%.5g',iter,sdev))
if sdev<0.00001
break
end
end
function u = tridag(a,b,c,r,n)
bet=b(1);
u(1)=r(1)/bet;
for j=2:n
gam(j)=c(j-1)/bet;
bet=b(j)-a(j)*gam(j);
u(j)=(r(j)-a(j)*u(j-1))/bet;
end
for j=n-1:-1:1
u(j)=u(j)-gam(j+1)*u(j+1);
end
Soution of tridiagonal system by factorization
Estimated time step

## Slide 34
Post processing (velocities, viscosities, BC for vorticity) UVMBC.m
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 
for i=2:nx-1
for j=2:ny-1
v(i,j)=-(psi(i+1,j)-psi(i-1,j))/(2*hx)*dksidx(i,j)-(psi(i,j+1)-psi(i,j-1))/(2*hy)*detadx(i,j);
u(i,j)=(psi(i,j+1)-psi(i,j-1))/(2*hy)*detady(i,j);
end
end
for i=2:nx-1
for j=2:ny-1
dudx(i,j)=(u(i+1,j)-u(i-1,j))/(2*hx)*dksidx(i,j)+(u(i,j+1)-u(i,j-1))/(2*hy)*detadx(i,j); dudy(i,j)=(u(i,j+1)-u(i,j-1))/(2*hy)*detady(i,j);
dvdx(i,j)=(v(i+1,j)-v(i-1,j))/(2*hx)*dksidx(i,j)+(v(i,j+1)-v(i,j-1))/(2*hy)*detadx(i,j); dvdy(i,j)=(v(i,j+1)-v(i,j-1))/(2*hy)*detady(i,j);
end
end
for i=2:nx-1
for j=2:ny-1
mju(i,j)=K*(2*dudx(i,j)^2+2*dvdy(i,j)^2+(dudy(i,j)+dvdx(i,j))^2)^((n-1)/2);
end
end
for i=2:nx-1
for j=2:ny-1
dmjudx(i,j)=(mju(i+1,j)-mju(i-1,j))/(2*hx)*dksidx(i,j)+(mju(i,j+1)-mju(i,j-1))/(2*hy)*detadx(i,j); dmjudy(i,j)=(mju(i,j+1)-mju(i,j-1))/(2*hy)*detady(i,j);
end
end
for i=1:nx
dmjudx(i,1)=dmjudx(i,2); dmjudx(i,ny)=dmjudx(i,ny-1);
end
for j=1:ny
dmjudx(1,j)=dmjudx(2,j); dmjudx(nx,j)=dmjudx(nx-1,j);
end
rlx=0.5;
for i=1:nx
omega(i,1)=omega(i,1)*(1-rlx)+rlx*2*psi(i,2)/hy^2*detady(i,1)^2;
omega(i,ny)=omega(i,ny)*(1-rlx)+rlx*2*(psi(i,ny-1)-psiw)/hy^2*(detadx(i,ny)^2+detady(i,ny)^2;
end

## Slide 35
Decomposition extrastress on the elastic and viscous component
For comparison
It is only an approximation of the corresponding constant viscosity
Transport equations for vorticity (right side of the resultant elastic strain). From a purely hyperbolic transport equation is zero Re turned out nice for elliptic equations  (LAD - LAplacian Driven)
Decomposition viscous stress tensor for purely viscous component (described by model GNF - Generalised Newtonian Fluid) and the elastic component sij is apparently purposeless, but has the advantage that it leads to an equation in which the vorticity  dominates even at zero Re.
Kontroloval: zitny

## Slide 36
Decomposition extrastress on the elastic and viscous component (variable µ9
The variable viscosity (non-zero first and second derivatives of viscosity). In addition Laplacian vorticity there appears a number of terms (partial derivatives of velocity)
Kontroloval: zitny
Neglecting second derivatives of viscosity (even the first derivatives are highly discontinuous and could be causing problems during solution)

## Slide 37
Transformation vorticity into computational domain
Transport equation for vorticity (variable viscosity)
material derivative of streamline
Kontroloval: zitny

## Slide 38
Discretized vorticity – central differences
Right hand size Gij is nonzero only for nozero stresses
Kontroloval: xxxxxx

## Slide 39
Discretised vorticity – upwind dif. at dominated convective transport
Interpretation of these velocity components is not immediately apparent (may be negative)
Comparing the size of the convective and diffusive member
Kontroloval: xxxxxx

## Slide 40
Boundary conditions – vorticity
The boundary conditions for vorticity resulting from the requirement of zero velocity on the wall u = v = 0 =0, 1
It follows from these equations that the first partial derivative must be zero in physical and computational plane. In the computational plane complete quadratic polynomial will replace the stream function around a node on the wall
Six polynomial coefficients should ensure 4 values in nodes and two conditions of zero derivatives at point i,Ny. Coefficients of coordinates  are zero.
=1 Gaussian wall
=0 plain wall
i,j=Ny


=0
=1
=0
=2
hy
i,Ny-1
i,j=1
Kontroloval: xxxxxx

## Slide 41
Boundary conditions – vorticity
Substituting the definition of a polynomial we get a strong vorticity boundary condition at Gaussian wall
Strong boundary condition at the bottom wall
Boundary conditions for ,  at input and output expect stabilized velocity profile
x
y
H
=0
=1
Velocity profile at inlet (for y<H*/2)
where um is the maximum velocity in the flow channel axis (width H) corresponding to a power law fluid flow index n
Kontroloval: xxxxxx
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 42
Boundary conditions – stream function and vorticity
Boundary conditions for ,  at inlet and outlet with gap thickness
Overall flowrate
Stream function at inlet
Vorticity at inlet and outlet
Approximation valid only for fully developed velocity profile
is the boundary condition for  at upper wall (w=0 at bottom wall)
Kontroloval: xxxxxx

## Slide 43
Iterative solution of  OMG.m
OMG
Nodal velocities and boundary conditions for ()
i=2..Nx-1
Solution of tridiagonal systém for  in vertical direction i. (upwind)
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 44
In a similar way like solution of stream function we separate discretized algebraic equations for vorticity to the time marching solution consisting in horizontal sweep (time step dt1) and vertical sweep (time step dt2).
Iterative solution of  (OMG.m)
Previously derived transport by pseudovelocities and implementation of upwind

## Slide 45
Iterative solution of  OMG.m
%vorticity
omegaold=omega;
for iter=1:20
%vertical sweep
for i=2:nx-1
aa(1)=0;bb(1)=1;cc(1)=0;dd(1)=omega(i,1); aa(ny)=0;bb(ny)=1;cc(ny)=0;dd(ny)=omega(i,ny);
for j=2:ny-1
vx=(rho*u(i,j)-2*dmjudx(i,j))*dksidx(i,j); vy=(rho*v(i,j)-2*dmjudy(i,j))*detady(i,j)+mju(i,j)*detadxdx(i,j);
Vxp=(vx+abs(vx))/(2*mju(i,j)*hx); Vxn=(vx-abs(vx))/(2*mju(i,j)*hx); Vyp=(vy+abs(vy))/(2*mju(i,j)*hy); Vym=(vy-abs(vy))/(2*mju(i,j)*hy);
G1=q1(i,j)/hy^2*(syy(i,j+1)-sxx(i,j+1)-2*(syy(i,j)-sxx(i,j))+syy(i,j-1)-sxx(i,j-1));
G2=q2(i,j)/(2*hy)*(syy(i,j+1)-sxx(i,j+1)-syy(i,j-1)+sxx(i,j-1));
G3=q3(i,j)/(4*hx*hy)*(syy(i+1,j+1)-sxx(i+1,j+1)+syy(i-1,j-1)-sxx(i-1,j-1)-syy(i+1,j-1)+sxx(i+1,j-1)-syy(i-1,j+1)+syy(i-1,j+1));
G4=q4(i,j)/(2*hy)*(sxy(i,j+1)-sxy(i,j-1)); G5=q5(i,j)/hx^2*(sxy(i+1,j)-2*sxy(i,j)+sxy(i-1,j)); G6=(q6(i,j)-q8(i,j))/hy^2*(sxy(i,j+1)-sxy(i,j)+sxy(i,j-1));
G7=q7(i,j)/(4*hx*hy)*(sxy(i+1,j+1)+sxy(i-1,j-1)-sxy(i-1,j+1)-sxy(i+1,jk-1)); Gij=G1+G2+G3+G4+G5+G6+G7;
aa(j)=-gyy(i,j)/hy^2+Vyp;
cc(j)=-gyy(i,j)/hy^2-Vym;
bb(j)=1/dt2+2*gyy(i,j)/hy^2-Vyp+Vym;
dd1=omega(i,j)/dt2+gxx(i,j)/hx^2*(omega(i-1,j)-2*omega(i,j)+omega(i+1,j)); dd2=Vxp*(omega(i,j)-omega(i-2,j))+Vxm*(omega(i+1,j)-omega(i,j));
dd3=gxy(i,j)/(4*hx*hy)*(omega(i+1,j+1)+omega(i-1,j-1)-omega(i+1,j-1)-omega(i-1,j+1)); dd(j)=dd1+dd2+dd3-Gij/mju(i,j);
end
omega(i,:)=tridag(aa,bb,cc,dd,ny);
end
sum=0;
for i=1:nx
for j=1:ny
sum=sum+abs(omega(i,j)-omegaold(i,j));
end
end
sdev=sum/(nx*ny)/psiw; disp(sprintf(' iter=%d relsum=%.5g',iter,sdev))
if sdev<0.00001
break
end
end

## Slide 46
Constitutive equations White Metzner.
Geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolické MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Nodal velocities and viscosity. BC for 
When you skip these three sections (iterative refinement of the stream function and vorticity) will result Pavlovec approximation of the solution, but for a smooth Gaussian gap profile.

## Slide 47
Constitutive equation White Metzner.
Kontroloval: xxxxxx

## Slide 48
Constitutive equation White Metzner. Boundary conditions (BC) at wall.
For upper curved wall
For bottom (planar) wall
System of 3 linear algebraic equations for 3 unknowns
At wall with transducers is syy=0 and yy =0.
It offers the possibility to integrate WM hyperbolic equations from left to right and bottom to top
Kontroloval: xxxxxx

## Slide 49
Transformation of constitutive equations White Metzner.
Kontroloval: xxxxxx

## Slide 50
Transformation of constitutive equations White Metzner (auxilliary variables)
Interpretation as material derivative (corresponding to motion of fluid particle along =konst)
Kontroloval: xxxxxx

## Slide 51
Discretized constitutive equation White Metzner (UP direction)
i,j


=0
=1
=0
=2
hy
i,j-1
i,j=1
i-1,j
Kontroloval: xxxxxx
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 52
Discretized constitutive equation White Metzner (UP direction).
Kontroloval: xxxxxx
Resulting system of algebraic equations for three stresses at point i,j evaluated from stresses at left and from bottom

## Slide 53
Discretized constitutive equation White Metzner (DOWN direction)
i,j


=0
=1
=0
=2
hy
i,j+1
i,j=1
i-1,j
Kontroloval: xxxxxx
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 54
Discretized constitutive equation White Metzner (DOWN direction).
Kontroloval: xxxxxx
Resulting system of algebraic equations for three stresses at point i,j evaluated from stresses at left and top

## Slide 55
Discretized constitutive equation White Metzner (iterative threediagonal)
i,j


=0
=1
=0
=2
hy
i,j+1
i,j=1
i-1,j
Kontroloval: xxxxxx
i,j-1

## Slide 56
Discretized constitutive equation White Metzner (iterative threediagonal)
Kontroloval: xxxxxx
Diagonal (vector bb) Low diagonal (vector aa) Upper diagonal (vector cc)
WM
iteration
stress sxx (3diagonal solver)
stress syy (3diagonal solver)
stress sxy (3diagonal solver)
BC for sxx, syy, sxy
i=2,3,…,nx
I section

## Slide 57
Discretized constitutive equation White Metzner MW.m (Matlab)
Kontroloval: xxxxxx
Resulting system of algebraic equations for three stresses at point i,j evaluated from stresses at left and from bottom

## Slide 58
Poisson equation for pressure
Decomposition to elastic and viscous components
Kontroloval: xxxxxx
geometry
Approximate profiles u,v, ,  for power law fluid
iteration
Elastic stress sxx, syy, sxy (hyperbolic MW)
Poisson equation for 
Poisson equation for 
Poisson equation for pressure p
Velocities, µ , BC for 

## Slide 59
Poisson equation for pressure
For constant viscosity
Kontroloval: xxxxxx
A sum of all the members in the viscosity coefficient is zero, therefore, the viscosity does not directly affect the relationship between the pressure and the elastic tension
For variable viscosity the relationship between the pressure and the elastic tension appear

## Slide 60
Poisson equation for pressure. Boundary conditions
Kontroloval: xxxxxx
The equation for pressure distribution is elliptic equation of second order, and in each point of the border is necessary to prescribe exactly one boundary condition: Either directly pressure (at least in one point, because the pressure field in an incompressible liquid is defined up to an arbitrary constant) or the normal derivative of the pressure (Neuman boundary condition of the second kind). At the inlet, where we assume the absence of elastic effects can be fixed e.g. zero pressure over the cross section (p = 0). The solid wall (u = v = 0) is required to enter a pressure gradient, starting from the Cauchy equilibrium equations